## Slide 1: Power System Design
Unit-2
Load flow Analysis

## Slide 2: Topic covered as:
Load flow problem
Ybus
Solution technique using Gauss seidel method

## Slide 3: Introduction of Load flow study
It is also known as power flow study.
Load flow study in power system is the steady state solution of the power system network.
It is a steady –state analysis whose target is to determine the following
  Bus voltage
  Branch current
  Real and reactive power flows in a system under a given load conditions

## Slide 4
Load flow study is done on a power system to ensure that:
  Generation supplies the demand (load) plus losses.
  Bus voltage magnitudes remains close to rated values.
  Generation operates within specified real and reactive power limits
  Transmissions lines and transformers are not overloaded.

## Slide 5: Bus admittance matrix).
Bus admittance matrix is often used in solving load flow problem
Node-voltage equation is
Here, =vector of injected bus current.
= Vector of bus Voltage,
= Bus admittance matrix.
Diagonal element is known as self admittance of bus
Off -Diagonal element is known as transfer admittance of bus
Spars matrix
Symmetric matrix here,
if ith and kth bus are not connected .
Dimension (n x n) where n is the number of buses

## Slide 6: 4 bus system

## Slide 7: Equivalent ckt. of 4 bus system

## Slide 8: Applying KCL in 4 bus system and arrange equation in matrix form

## Slide 10
Node-voltage equation is
here, =vector of injected bus current.
= Vector of bus Voltage,
= Bus admittance matrix.
, i=1,2,3,…..n

## Slide 11: Types of bus in load flow problem
There are three types of bus:
  Slack bus /swing bus/Reference bus
  PV bus/voltage controlled bus
  PQ bus
Bus type | No. of bus | Quantities specified | Quantities unknown
Slack bus 1 | 1 |  | 0
PV bus 2,3,---m | m-1 | P, | 
PQ bus m+1,…..n | n-m | P,Q | 
Bus type | No. of bus | Quantities specified | Quantities unknown
Slack bus 1 | 1 |  | 0
PV bus 2,3,---m | m-1 |  | 
PQ bus m+1,…..n | n-m | P,Q | 

## Slide 12: Power flow problem
=Injected Current at bus ‘i’
, i=1,2,3,…..n
= Injected real power at bus ‘i’
= Injected reactive power at bus ‘i’

## Slide 14: Gauss-seidel method for load flow
It is an iterative algorithm for solving a set of non linear algebraic equation.
The value is updated each iteration.
let n –bus system having 1-slack bus, 2,3,4…to m –PV bus and (m+1)….n-PQ bus.
are specified in Slack bus
P , are known and is unknown in PV bus, but condition is If condition is violated this bus is treated as PQ bus during that iteration.
P,Q are known in P-Q bus and and are unknown.

## Slide 15
=scheduled injected real power at bus ‘i’
= generated real power at bus ‘i’
= demand (load) power at bus ‘i’
=scheduled injected reactive power at bus ‘i’
= generated reactive power at bus ‘i’
= demand (load) reactive power at bus ‘i’

## Slide 16: Algorithms for Gauss Seidel method (without Q limit)
Let flat start =
Set max iter
Calculate
For PV bus i=2,3…m
=angle ()
=

## Slide 17
For PQ bus i=m+1,……n
and
Increase iter count,t=t+1
Go to step 3 if t< max iter
end

## Slide 18: Algorithms for GS method(with Q limit)
Let flat start =
Set max iter
Calculate
For PV bus i=2,3…m
=angle ()
= if

## Slide 19
if <
if
For PQ bus i=m+1,……n
and
Increase iter count,t=t+1
Go to step 3 if t< max iter
end

## Slide 21
Thank You